## Slide 1
4 The Medium Access Control Sublayer

## Slide 2: High Lights
Channel allocation algorithms
Contention：ALOHA,S-ALOHA,CSMA,CSMA/CD
Collision-Free Protocols : bit-map, binary countdown, Token
Limited-Contention Protocols
LAN
IEEE802.3, HIGH-SPEED LANS (802.3u)
Gigabit Ethernet(802.3z)
IEEE802.11(WLAN) LLC(802.2)
BRIDGE: transparent bridge
REPEATER,HUB, BRIDGE,SWITCH,ROUTER
VLAN

## Slide 3
4.1 The Channel Allocation Problem

## Slide 4
M/M/1 System

## Slide 5: M/M/1 System
incoming number is K in period T
λ: mean arrival rate (frames/sec)
1/μ: mean frame length (bits/frame)
C: data transmission rate, channel capacity (bits/sec) , the service rate is µC frames/sec
mean time delay

## Slide 6: M/M/1 Example
λ=200 μC=250
T=1/(250-200)=20ms

## Slide 7: The Channel Allocation Problem
Static Channel Allocation in LANs and MANs
Dynamic Channel Allocation in LANs and MANs

## Slide 8
Static Channel Allocation

## Slide 9: Static Channel Allocation
  Divide the single channel into N (TDM or FDM) independent subchannels, each channel capacity
  mean arrival rate
  mean time delay

## Slide 10: Static Channel Allocation(2)
Single channel
  C is 100 Mbps
  Mean frame length, 1/µ, is 10,000 bits
  µC=10000 frames/sec
  Frame arrival rate is 5000 frames/sec
  Mean delay = 200 µsec
Divide the channel into N
  Replace the 100-Mbps network with 10 networks of 10 Mbps each and statically allocate each user to one of them
  Mean delay = 2 msec

## Slide 11
Dynamic Channel Allocation

## Slide 12: Classification of Dynamic Channel Allocation
Controlled multiple access
  Centralized: polling
  Decentralized: token
Random multiple access
  ALOHA
  CSMA, CSMA/CD, CSMA/CA

## Slide 13: Five Key Assumptions of Dynamic Channel Allocation
Station Model
Single Channel Assumption.
Collision Assumption
(a) Continuous Time.
(b) Slotted Time.
(a) Carrier Sense. (b) No Carrier Sense.

## Slide 14: Station Model.
  N independent stations, generates frames for transmission
  The probability of a frame being generated in an interval of length t is λt, where λ is a constant (the arrival rate of new frames).
  Once a frame has been generated, the station is blocked and does nothing until the frame has been successfully transmitted

## Slide 15: Single Channel Assumption
  A single channel is available for all communication
  All stations can transmit on it and all can receive from it
  All stations are equivalent, although protocol software may assign priorities to them.

## Slide 16: Collision Assumption
  If two frames are transmitted simultaneously, they overlap in time and the resulting signal is garbled
  All stations can detect collisions
  A collided frame must be transmitted again later

## Slide 17: Continuous Time &Slotted Time.
  Continuous Time
  Frame transmission can begin at any instant
  Slotted Time
  Time is divided into discrete intervals (slots).
  Frame transmissions always begin at the
  start of a slot.
    A slot may contain 0, 1, or more frames, corresponding to an idle slot, a successful transmission, or a collision, respectively.

## Slide 18: Carrier Sense
  Stations can tell if the channel is in use before trying to use it. If busy, no station will attempt to use it until it goes idle.
  No Carrier Sense. Stations cannot sense the channel before trying to use it. They just go ahead and transmit. Only later can they determine whether the transmission was successful

## Slide 19
4.2 Multiple Access Protocols

## Slide 20: Multiple Access Protocols
ALOHA
Carrier Sense Multiple Access Protocols
Token
Collision-Free Protocols
Limited-Contention Protocols
Wireless LAN Protocols

## Slide 21
ALOHA

## Slide 22: Pure ALOHA
In pure ALOHA, frames are transmitted at completely arbitrary times.

## Slide 23: Pure ALOHA Model
Each station transmit frames arbitrarily
If collision occurs, the sender waits a random time and sends it again
N
N-1
2
1
interface
Bus channel
The model of ALOHA

## Slide 24: Pure ALOHA: Collision Demo(1)
Collision reason：two station send frame simultaneously
1
2
N-1
N
...

## Slide 25: Pure ALOHA: Collision Demo(2)
A1
new frame
B1
A2
A2
B1
collison
t1
t2
B2
A2
t3
B2
t4
B3
A3
station A
Station B
Final effect
A1
B1
A2
B2
t
t
t

## Slide 26: Pure ALOHA:Performance Analysis(1)
Vulnerable period for the shaded frame.

## Slide 27: Pure ALOHA: Performance Analysis(2)
Assumptions
  Fixed frame length, frame time is t
  Frames generated according to Poisson distribution
  New frames and retransmitting frames also accord to Poisson distribution
Parameters
  Throughput S: mean successful frames per frame time 0 S  1
  Network load G: mean frames per frame time G≥S
  probability P0: successful transmission
S = G  P0

## Slide 28: Pure ALOHA: Performance Analysis(3)
P0= P [no other traffic being initiated during the entire vulnerable period] = e –λ(2T) = e –2G
[ P=(λT)K e-λt/K!]
Throughput: S = G  P0 = G e -2G
Maximum throughput occurs when G=0.5, S=1/2e ≈ 0.184

## Slide 29: Slotted ALOHA
Principle
  Divide time into discrete intervals, each interval corresponding to one frame, so each user must know slot boundaries (synchronization)
A1
new frame
B3
A2
A2
B1
collision
t1
t2
B2
B2
B3
A3
station B
final effect
A1
B1
A2
B2
A3
station A

## Slide 30: Slotted ALOHA(2)
T
Tx
P0= P [ arrival interval > T ] = e - λ T = e –G
Throughput S = G  P0 = G e -G
Maximum throughput occurs when G=1, S=1/e ≈ 0.368
[ P=(λT)K e-λT/k!= =GK e-G/k!]
When G=1
37%: Slots empty
37%: Successes
26%: Collisions

## Slide 31: ALOHA Summary
Throughput versus offered traffic for ALOHA systems.

## Slide 32: Expected number of transmissions
Pure ALOHA
  P0=e-2G
  Pk=e-2G(1-e-2G)k-1
  E= kPk=e2G
Slotted ALOHA
  P0=e-G
  Pk=e-G(1-e-G)k-1
  E= kPk=eG
Higher values of G reduces number of empties but increases number of collisions exponentially

## Slide 33
Carrier Sense Multiple Access Protocols (CSMA)

## Slide 34: CSMA protocols
Station listens for a carrier before Sending
Classification
  1-persistent CSMA
    If the channel is busy, waits until it becomes idle, then transmits frame immediately,
    If a collision occurs, waits for a random amount of time and start all over again.
  Nonpersistent CSMA
    if the channel is busy, waits for a random amount of time and sense channel again

## Slide 35: CSMA protocols
  P-persistent CSMA (slotted channel)
    If the channel is busy, waits to the next slot
    If idle, transmits frame with probability of p, with a probability of q=1-p it defers to the next slot
    Repeated until either the frame has been transmitted or another station has begun transmitting
    If there had been a collision, waits a random time and starts again

## Slide 36: CSMA Comparison
  1-persistent CSMA
    Low delay when low load
    Low throughput when high load
  Nonpersistent CSMA
    High throughput when high load

## Slide 37: Persistent and Nonpersistent CSMA
Comparison of the channel utilization versus load for various random access protocols

## Slide 38: CSMA Collision Reasons
Station A
Station B

B detects an idle channel
A detects
an idle channel
:Propagation time between A and B
1. Two or more stations sense the channel to be idle and begin transmitting
2. Propagation time : 
e,

## Slide 39: CSMA with Collision Detection（CSMA/CD）
Principle
  Station aborts the transmission as soon as it detects a collision, it saves time and bandwidth
1-persistent CSMA/CD
  When a station sense the channel idle, send immediately and keep on sensing, when collision occur, abort transmission immediately

## Slide 40: CSMA/CD: Channel state
CSMA/CD can be in one of three states: Contention, Transmission, or Idle.

## Slide 41: CSMA/CD: Contention period
Station A
Station B

B sense collision
A sense collision
B sense idle
TB
2 
2
contention period =
TB<= 
: single trip propagation
2

## Slide 42: CSMA/CD: Contention period(2)
CSMA/CD with a single channel is inherently a half-duplex system

## Slide 43
Collision-Free Protocols

## Slide 44: Basic bit-map protocol
Principle
  Each contention period consists of N slots (bits), with each station use one slot
  If station have frames to send, it reserve it by fill ‘1’ in its slot, (reservation protocols)

## Slide 45: Bit-map protocol: Performance
N station, contention time is N
One data frame is d bits, so time is d
Low load
  Efficiency= d/(N+d)
High load
  All stations have frames to send, so the N bits contention period prorated over N frames, yielding an 1 bit overhead per frame
  Efficiency=d/(d+1)

## Slide 46: Token Ring

## Slide 47: Properties
The ring is a single, shared medium All nodes see all frames.
A distributed algorithm determines when a node can transmit.
Data always flows in one direction.
Basic idea: A token circulates around the ring. When a host has a frame to transmit, it seizes the token and injects the frame on the medium. The frame is forwarded by intermediate nodes until arriving at the destination. The destination puts the frame back after receiving it, but with a “special mark”. The frame circulates back to the sender.

## Slide 48
令牌环 操作
A
T
T = 0
T
A
T
Data
C
T
Data
C
T
Data
C
T
Data
C
A
B
C
D
D
B
C
B
C
D
A准备截获令牌
A发数据
A释放令牌
T = 0
T = 1
A
A
A

## Slide 49: Protocol of token
Token ring
  802.5
Token bus
  802.4

## Slide 50: binary countdown protocol
Problem
  Basic bit-map protocol: the overhead is 1 bit per station
  It does not scale well to networks with thousands of stations
  Solution：Using binary station addresses
Principle
  Each station wanting to use the channel broadcast its address as a binary bit string
  The bits in each address position from different stations are BOOLEAN ORed together
Efficiency
  d/(log2N+d)
Disadvantage
  high-numbered station always gets high priority to send
  Variation: set the lowest priority to the station which send successfully in the last contention

## Slide 51: Binary Countdown protocol
A dash indicates silence

## Slide 52
Limited-Contention Protocols

## Slide 53: Limited-Contention Protocols
Basic strategies for channel acquisition
  Contention:CSMA/CD
  Collision-free methods: Bit-map
Performance measures
  Delay at low load
  Channel efficiency at high load

## Slide 54: Performance of Symmetric Contention
The probability of some station acquiring the channel can be increased only by decreasing the amount of competition
P=1/k, A=(k-1/k)k – 1
Acquisition probability for a symmetric contention channel

## Slide 55: Limited-Contention Protocols
Limited-contention protocols
  Use contention at low load, use a collision-free technique at high load
  Divide stations into groups, each station contends the group’s slot

## Slide 56: Adaptive Tree Walk Protocol
depth search first
  build a binary tree with stations as the leaves
  all stations contend slot 0
  if no collision, ok
  else only stations falling under node 2 compete slot 1
Slot 1
Slot 0

## Slide 57: Improvements to Adaptive Tree Walk Protocol
Level 0
Level 1
Level 2
Level 3
1
2
3
4
5
6
7
A
B
C
D
E
F
G
H
station
Slot 0
slot1
Slot 2
Slot 3
slot4
G and H being the only ones wanting to transmit

## Slide 58
Wireless LAN Protocols

## Slide 59: Problems
Radio transmitter & receiver
  Radio transmitters have some fixed range.
  In some wireless LANs, not all stations are within range of one another
  Interference at the receiver, not at the sender
  CSMA/CD is not appropriate
Hidden station problem
Exposed station problem
(a) A transmitting (b) B transmitting

## Slide 60: Solutions
PCF (Point Coordination Function)
  Uses the base station to control all activity in its cell
  Base station broadcasts a beacon frame periodically
  The beacon frame contains system parameters. It also invites new stations to sign up for polling service
  Once a station has signed up, it is effectively guaranteed a certain fraction of the bandwidth
DCF (Distributed Coordination Function)
  CSMA/CA:CSMA with Collision Avoidance, MACA(Multiple Access with Collision Avoidance) protocol

## Slide 61: MACA: Collision Avoidance
RTS: Request To Send
CTS: Clear To Send
A sends an RTS frame to B (30 bytes, contains data length)
B replies with a CTS frame(contains data length from RTS)
Upon receipt of the CTS frame, A begins data transmission
Stations hearing RTS remain silent long enough (C,E)
Stations hearing CTS remain silent during the upcoming data transmission (D,E)

## Slide 62
4.3 Ethernet

## Slide 63: Bob Metcalfe’s Vision
  June 1976 National Computer Conference
  (INTEL had just developed 8080, running at 4.77M)
  Robert Metcalfe (1946~)
    1969 Graduated from MIT
    1973 Harward (Ph.D)
    1972~1979 Xerox PARC (Palo Alto Research Center)
      1973 Ethernet, 3Mbps
    1979~1990 3Com

## Slide 64: Early History
1973 | Xerox PARC begins development of bus topology LAN
1976 | Successful CSMA/CD system to connect 100 workstations on 1 km cable
1980 | Digital Equipment Corp, Intel Corp, and Xerox release de-facto Ethernet DIX standard
1980 | IEEE 802 Standardization process begins
1983 | IEEE 802.3 Standard Published

## Slide 65: Ethernet
Ethernet Cabling
Manchester Encoding
Ethernet MAC Sublayer Protocol
Binary Exponential Backoff Algorithm
Ethernet Performance
Switched Ethernet
Fast Ethernet
Gigabit Ethernet
10 Gigabit Ethernet
Retrospective on Ethernet

## Slide 66
Ethernet Cabling

## Slide 67: Ethernet Cabling
The most common kinds of Ethernet cabling.

## Slide 68: Ethernet Cabling:AUI,BNC,UTP5
Three kinds of Ethernet cabling.
(a) 10Base5, (b) 10Base2, (c) 10Base-T.

## Slide 69: 10Base5: Thick Ethernet(1)
Cable
  Φ10, Coax, 500m
  Connections to it are generally made using vampire taps, in which a pin is very carefully forced halfway into the coaxial cable's core
Transceiver cable
  Connects the transceiver to an interface board in computer
  Up to 50 meters long
  Contains five individually shielded twisted pairs
    Two of the pairs are for data in and data out
    Two more are for control signals in and out
    The fifth pair, not always used, allows the computer to power the transceiver electronics

## Slide 70: 10Base5: Thick Ethernet(2)
Interface board
  Transmits and receives frames, assembling data into proper frame format, processing checksums
  Manage a pool of buffers for incoming frames, a queue of buffers to be transmitted, direct memory transfers with the host computers
Transceiver
  Handle carrier detection and collision detection
  For collision, puts a special invalid signal on cable to ensure that all other transceivers also realize that a collision has occurred

## Slide 71: 10Base2: Thin Ethernet
Cable: Φ5, Coax, 185m
BNC T-junction connector
Transceiver electronics are on the controller board

## Slide 72: 10BaseT
10Base-T: No shared cable at all
HUB
  Station is connected to HUB by a dedicated cable (Max 100m)
  A box full of electronics
    物理上星状结构，逻辑上总线结构
    任意站发送，所有站接收
  媒体信号的再生（放大和整形）
RJ-45, 5 UTP (Unshielded Twisted Pairs)
  两对线，分别用于收和发
  差分传输：减少电磁干扰
  同一线对的绞合：减少近端串扰
3UTP
STP: Shielded Twisted Pairs

## Slide 73: Using Hubs to Enlarge a LAN

## Slide 74: Ethernet Topologies
(a) Linear, (b) Spine
(c) Tree, (d) Segmented.

## Slide 75
Manchester Encoding

## Slide 76: Manchester Encoding
(a) Binary encoding
(b) Manchester encoding
(c) Differential Manchester encoding

## Slide 77
Ethernet MAC Sublayer Protocol

## Slide 78: Ethernet MAC Sublayer Protocol
Frame formats. (a) DIX Ethernet, (b) IEEE 802.3.
Type ( 0806:ARP, 0800:IP 8137:IPX)

## Slide 79: Ethernet address

## Slide 80: Frame length
Maximum frame length
  1514 byes (Data length 1500 bytes)
  Based on the fact that a transceiver needs enough RAM to hold an entire frame and RAM was expensive in 1978
Minimum frame length
  Valid frames must be at least 64 bytes long
  If data portion is less than 46 bytes, Pad field is used to fill out the frame to the minimum size
  Prevent a station from completing the transmission of a short frame before the first bit has even reached the far end of the cable, where it may collide with another frame
    network speed
    maximum cable length

## Slide 81: Minimum frame length

## Slide 82: Binary Exponential Backoff Algorithm
time slots length: 512 bit times (51.2 µsec)
1st collision, random number 0~1
2nd collision, random number 0~3
….
9th collisoin, random number 0~511
10th collisoin, random number 0~1023
11th collisoin, random number 0~1023
…
16th collisoin, random number 0~1023
After 16 collisions, reports failure to computer
Further recovery is up to higher layers

## Slide 83: IEEE 802.3 Performance
Frame length: F
Bandwith: B
Cable length: L
Speed of signal propagation: c
1
channel efficency =
1+2BLe/cF

## Slide 84: Ethernet Performance
Efficiency of Ethernet at 10 Mbps with 512-bit slot times

## Slide 85
Switched Ethernet

## Slide 86: Switched Ethernet
High-speed backplane
Collision domain
  With only one station per collision domain, collisions are impossible and performance is improved

## Slide 87
Fast Ethernet

## Slide 88: 802.3u: A Soaped-up Ethernet
The need to be backward compatible with existing Ethernet LANs
The fear that a new protocol might have unforeseen problems
The desire to get the job done before the technology changed

## Slide 89: Fast Ethernet
Keep all the old frame formats, interfaces, and procedural rules
Reduce the bit time from 100 ns to 10 ns
Reducing maximum cable length by a factor of 10
All fast Ethernet systems use hubs and switches; multidrop cables with vampire taps or BNC connectors are not permitted

## Slide 90: Fast Ethernet cabling

## Slide 91: 100Base-T4
Uses a signaling speed of 25 MHz
Requires 4 twisted pairs (category 3 UTP)
  One is always to the hub
  One is always from the hub
  The other two are switchable to the current transmission direction
Coding
  Manchester encoding is not used
  Ternary signals are sent during a clock period
    27 possible symbols, transmit 4 bits
  At least 33.3-Mbps reverse channel(8B/6T)

## Slide 92: 100Base-TX
Uses a signaling speed of 125 MHz
Requires 2 twisted pairs (category 5 UTP)
  One is to the hub
  One is from the hub
  (Full duplex)
Coding
  4B/5B: 125 * 4/5 = 100Mbps

## Slide 93: Interconnection Devices
Hub (Half-duplex communication)
  Incoming lines are logically connected, forming a single collision domain
  All the standard rules, including the binary exponential backoff algorithm, apply, so the system works just like old-fashioned Ethernet
  Hubs are not permitted with 100Base-FX
Switch
  Incoming frame is buffered and passed to the destination
  100Base-FX cables are too long for collision algorithm, must be connected to switches

## Slide 94: 10-Mbps & 100-Mbps Autoconfiguration
802.3u provides a way for two stations to negotiate the speed (10 or 100 Mbps) and duplexity (half or full)
Most fast Ethernet products use this feature to autoconfigure themselves

## Slide 95
Gigabit Ethernet

## Slide 96: 802.3z Goals
Make Ethernet go 10 times faster
Remain backward compatible with all existing Ethernet standards
  Unacknowledged datagram service with both unicast and multicast
  Use 48-bit addressing scheme already in use
  Maintain the same frame format, including the minimum and maximum frame sizes

## Slide 97: Gigabit Ethernet
A two-station Ethernet.
A multistation Ethernet.

## Slide 98: Switch : Full-duplex Mode
Switch (Full-duplex Mode)
  Since no contention is possible, the CSMA/CD protocol is not used
  Maximum length of the cable is determined by signal strength issues
  Switches are free to mix and match speeds. Autoconfiguration is supported

## Slide 99: Hub: Half-duplex Mode
Simulating classic Ethernet
  Electrically connects all the lines internally
  Collisions are possible, so CSMA/CD protocol is required
Problem: A radius of 25 meters
Solutions
  Carrier extension
    Add padding after the normal frame to extend the frame to 512 bytes (Padding is added by the sending hardware and removed by the receiving hardware)
  Frame bursting
    Allows a sender to transmit a concatenated sequence of multiple frames in a single transmission
  Remain the radius of the network to 200 meters

## Slide 100: Gigabit Ethernet cabling

## Slide 101: Flow Control
Problem: 1 Gbps is quite fast
  If a receiver is busy with some other task for 1 ms, 1953 frames may have accumulated
  When a computer is shipping data to a computer on a classic Ethernet, buffer overruns are very likely
Control frames
  One end sending a special control frame to the other end telling it to pause for some period of time
  Normal Ethernet frames containing a type of 0x8808
  The first two bytes of the data field give the command; succeeding bytes provide the parameters.
Flow control
  PAUSE frames are used, 512ns~33.6ms

## Slide 102: Reasons for Longevity of Ethernet
Reliable
  10base2:BNC
  10BaseT
Cheap
  Thin Ethernet and twisted pair wiring is relatively inexpensive
  Interface cards are also low cost
Easy to maintain
  No software to install
  No configuration tables to manage
  Adding new hosts is as simple as just plugging them in

## Slide 103
10 Gigabit Ethernet

## Slide 104: Where to be needed
Inside data centers
Exchanges to connect high-end routers, switches, and servers
In long-distance, high bandwidth trunks between offices
The long distance connections use optical fiber, while the short connections may use copper or fiber

## Slide 105: Kind of 10-gigabit Ethernet
Support only full-duplex operation
Interfaces autonegotiate
64B/66B code

## Slide 106
4.4 Wireless LAN

## Slide 107
802.11/WIFI

## Slide 108: 802.11 LAN architecture
wireless host communicates with base station
  base station = access point (AP)
Basic Service Set (BSS)
  wireless hosts
  access point (AP): base station
  ad hoc mode: hosts only
BSS 1
BSS 2
Internet
Switch or router
AP
AP

## Slide 109: 802.11 protocol stack

## Slide 110: IEEE 802.11 Wireless LAN
802.11b
  2.4-5 GHz unlicensed radio spectrum
  up to 11 Mbps
  direct sequence spread spectrum (DSSS) in physical layer
  widely deployed, using base stations
802.11n
  up to 600 Mbps
  MIMO
802.11a
  5-6 GHz range
  up to 54 Mbps
  OFDM
802.11g
  2.4-5 GHz range
  up to 54 Mbps
  OFDM, like ADSL modem
All use CSMA/CA for multiple access
All have base-station and ad-hoc network versions

## Slide 111: IEEE 802.11: multiple access
avoid collisions: nodes transmitting at same time
802.11: CSMA - sense before transmitting
  don’t collide with ongoing transmission by other node
802.11: no collision detection!
  difficult to receive (sense collisions) when transmitting due to weak received signals (fading)
  can’t sense all collisions in any case: hidden terminal
  goal: avoid collisions: CSMA/C(ollision)A(voidance)

## Slide 112: CSMA/CA
802.11 MAC is different from that of Ethernet
  Radios are always half duplex
  Received signal is 106 times weaker than the transmitted, collision detection mechanism does not work
Avoid collisions with a protocol called CSMA/CA
  When a station has a frame to send:
  Waits until the channel is idle by sensing and wait DIFS
  Random backoff (0~15 time slots): counts down idle slots, pausing when frames are sent. Sends its frame when the counter reaches 0
  If the frame gets through, destination sends a short ACK
  Lack of an ACK is inferred to indicate a collision or other error, doubles the backoff period and tries again (as exponential backoff in Ethernet)
Notes: StandardSIFS(μs)IEEE 802.11b 10 IEEE 802.11a 16 IEEE 802.11g 10
DIFS = SIFS + (2 * Slot time)
StandardSlot Time(µs)DIFS(µs)IEEE 802.11b 20 50 IEEE 802.11a 9 34 IEEE 802.11g 9 or 20 28 or 50 PIFS = SIFS + Slot time
StandardSlot time(µs)PIFS(µs)IEEE 802.11b2030IEEE 802.11a925IEEE 802.11g9 or 2019 or 30

## Slide 113: CSMA/CA

## Slide 114: Channel Sensing
Physical sensing
  Checks the medium to see if there is a valid signal
Virtual sensing
  Each station keeps a logical record of when the channel is in use by tracking NAV (Network Allocation Vector)
  Each frame carries a NAV
    NAV of a data frame includes the time needed to send ACK
  Optional RTS/CTS mechanism

## Slide 115: 802.11 reliability
Lower the transmission rate
A fragment burst
.

## Slide 116: 802.11 Saving power
Beacon frames
  Clients can enter power-save mode;
  AP will buffer traffic;
  the client sends a poll message to the AP
APSD (Automatic Power Save Delivery)
the AP buffers frames and sends them to a client just after the client sends frames to it

## Slide 117: QOS:Interframe Spacing (IFS) in 802.11
DIFS (DCF) :Regular data frames
SIFS allow the parties in a single dialog
  ACK frame
  Other control frame sequences like RTS and CTS
  A burst of fragments
AIFS1 (Arbitration InterFrame Space)
  PCF, Voice or other high-priority traffic
AIFS4 used for background traffic

## Slide 118: QOS:TXOP
Two stations: 6Mbps and 54M bps
They each get to send one frame, both get 5.4Mbps on average
Use TXOP
They get 3 Mbps and 27 Mbps, respectively

## Slide 119: MAC Layer Frames
Data Frames
Control Frames
  RTS,CTS,ACK
Management Frames
  Beacon and Probe frames

## Slide 120: Format of the 802.11 Data Frame

## Slide 121: 802.11 frame: addressing
frame
control
duration
address
1
address
2
address
3
payload
CRC
2
2
6
6
6
2
0 - 2312
4
seq
control
Address 2: MAC address
of wireless host or AP
transmitting this frame
Address 1: MAC address
of wireless host or AP
to receive this frame
Address 3: MAC address
of router interface to which AP is attached

## Slide 122
Internet
router
AP
H1
R1
AP MAC addr H1 MAC addr R1 MAC addr
address 1
address 2
address 3
802.11 frame
R1 MAC addr AP MAC addr
dest. address
source address
802.3 frame
802.11 frame: addressing

## Slide 123
802.2: Logical Link Control

## Slide 124: 802.2: LLC
Run on top of 802.3 & other 802 protocols
  Hides differences between the various kinds of 802 networks by providing a single format and interface to the network layer
LLC provides three service options
  Unreliable datagram service
  (best-efforts datagram service)
  Acknowledged datagram service
  (Error-controlled)
  Reliable connection-oriented service
  (Error-controlled & flow-controlled)

## Slide 125: Position of LLC
(a) Position of LLC. (b) Protocol formats.

## Slide 126
4.8 Data Link Layer Switching

## Slide 127: Data Link Layer Switching
Bridges from 802.x to 802.y
Local Internetworking
Spanning Tree Bridges
Remote Bridges
Repeaters, Hubs, Bridges, Switches, Routers, Gateways
Virtual LANs

## Slide 128
Local Internetworking

## Slide 129: Data Link Layer Switching
The need for interaction
The organization may be geographically spread over several buildings
Split a single LAN into separate LANs to accommodate the load (multiple collision domains)
Physical distance(2500m)
Reliability
Security

## Slide 130: Bridge

## Slide 131: A LAN bridge from 802.11 to 802.3
Operation of a LAN bridge from 802.11 to 802.3.

## Slide 132: Bridges from 802.x to 802.y
Problems
  Each of the LANs uses a different frame format
  LANs do not run at the same data rate
  Different 802 LANs have different maximum frame lengths.
  Security: Wireless networks support encryption in the data link layer, Ethernet does not
  QoS (Quality of service：802.11、802.16)

## Slide 133: IEEE 802 frame formats

## Slide 134: A configuration with 4 LANs & 2 bridges

## Slide 135
Learning Bridge
（Transparent）

## Slide 136: Learning Bridge
Operates in promiscuous mode
  Accepting every frame transmitted on all the LANs to which it is attached
Station table
  Lists each possible destination and tell which output line (LAN) it belongs on
Routing procedure for an incoming frame
  If destination LAN and source LAN are the same, discard the frame
  If destination LAN and source LAN are different, forward the frame
  If destination LAN is unknown or multicast/broadcast address, use flooding algorithm
    Flooding algorithm: output on all the LANs to which the bridge is connected except the one it arrived on

## Slide 137: Station table: Backward Learning
Init
  When the bridges are first plugged in, all the hash tables are empty
Add
  Bridges operate in promiscuous mode, so they see every frame sent on any of their LANs
  By looking at the source address, they can tell which machine is accessible on which LAN

## Slide 138: Dynamic topologies
Problem
  The topology can change as machines and bridges are powered up and down and moved around
Solution
  Whenever a hash table entry is made, the arrival time of the frame is noted in the entry
  Whenever a frame whose source is already in the table arrives, its entry is updated with the current time
  Periodically scan the hash table and purges all entries more than a few minutes old
    If a computer is unplugged from its LAN, moved around the building, and plugged in again somewhere else, within a few minutes it will be back in normal operation, without any manual intervention
    This algorithm also means that if a machine is quiet for a few minutes, any traffic sent to it will have to be flooded until it next sends a frame itself

## Slide 139: Example
MAC Intf
B2
B1
A
B
C
D
E
F
1
2
1
2
MAC Intf
…
…
…
…
B 1
B → A
A → B
A 1
F → C
F 2
A → B
A 1
F → C
F 2

## Slide 140: Example2
B1 B2
1 A send frame to C A 1 A 2
2 E send frame to A E 2 E 3
3 D send frame to E D 3
4 E move to LAN2
5 E send frame to A E 2 E 2

## Slide 141: Protocol processing at a bridge

## Slide 142
Spanning Tree Bridges

## Slide 143: Loops in the Topology
Problem
  To increase reliability, some sites use two or more bridges in parallel between pairs of LANs
  This arrangement introduces problems because it creates loops in the topology

## Slide 144: Spanning Tree Bridges
Solution (Radia Perlman, 1983)
  Bridges communicate with each other and overlay the actual topology with a spanning tree that reaches every LAN
  Using this spanning tree, there is exactly one path from every LAN to every other LAN, loops are impossible
  Some potential connections between LANs are ignored in the interest of constructing a fictitious loop-free topology
Radia Perlman 2009
(born 1951)

## Slide 145: Spanning Tree Bridges
(a) Interconnected LANs. (b) A spanning tree covering the LANs. The dotted lines are not part of the spanning tree.

## Slide 146: Spanning Tree Bridges

## Slide 147: 802.1d: Constructing the Spanning Tree
  Bridge periodically multicast a message out all of its ports, this message is not forwarded, it includes:
    an ID based on its MAC address
    ID of the root it believe to be
    the distance to root
  Chose the bridge with the lowest ID to be the root, after enough messages exchanged, all bridges will agree on the root
  Remembers the shortest path to root, if there are multiple equivalent paths, the path via bridge with lowest ID is chosen
  Turn off ports that are not part of the shortest path
  Algorithm continues to run during normal operation to automatically detect topology changes and update the tree

## Slide 148: Dynamic Topologies
BPDU (Bridge Protocol Data Unit)
  Bridge periodically multicast a message (MAC 01:80:c2:00:00:00) out all of its ports, this message is not forwarded, it includes:
  an ID based on its MAC address
  ID of the root it believe to be
  the distance to root
Root Bridge of Whole Net
  Chose the bridge with lowest ID to be the root, after enough messages exchanged, all bridges will agree on the root
Root Port of Every Bridge
  Remembers the shortest path to root, if there are multiple equivalent paths, the path via bridge with lowest ID is chosen
Algorithm continues to run during normal operation to automatically detect topology changes and update the tree

## Slide 149
Repeaters, Hubs, Bridges, Switches, Routers and Gateways

## Slide 150: Repeaters, Hubs, Bridges, Switches, Routers and Gateways
(a) Which device is in which layer.
(b) Frames, packets, and headers.

## Slide 151: Hubs, Bridges, Switches
(a) A hub. (b) A bridge. (c) A switch.
Bridges & Switchs
  Special-purpose VLSI chips lookup and update station table entry in a few microseconds
  Buffer space: if frames come in faster than they can be retransmitted, the switch may run out of buffer space and start discarding frames
  Cut-through switches

## Slide 152
Virtual LANs

## Slide 153: Virtual LANs
A building with centralized wiring using hubs and a switch.

## Slide 154: Virtual LANs
A building with centralized wiring using hubs and a switch.

## Slide 155: Reason for Virtual LANs
Broadcast storm
  LAN capacity is occupied by these frames
  Machines are crippled just processing and discarding all the frames being broadcast
Security
  Many departments have information that they do not want passed outside their department

## Slide 156: Virtual LANs
(a) Four physical LANs organized into two VLANs, gray and white, by two bridges.
(b) The same 15 machines organized into two VLANs by switches.

## Slide 157: VLAN ID
  In the switches, configuration tables tell which VLANs are accessible via which ports
    Every port is assigned a VLAN ID
      This method only works if all machines on a port belong to the same VLAN
    Every MAC address is assigned a VLAN ID
      When a frame arrives, the switch extracts the MAC address and look it up in a table to see which VLAN the frame came from
    Every layer 3 protocol or IP address is assigned a VLAN ID

## Slide 158: The IEEE 802.1Q Standard
Transition from legacy Ethernet to VLAN-aware Ethernet.
The shaded symbols are VLAN aware. The empty ones are not.

## Slide 159: 802.1Q: Frame formats
The 802.3 (legacy) and 802.1Q Ethernet frame formats.
  VLAN protocol ID (16 bits): 0x8100
  Pri (3 bits)
  CFI (1 bit)
  VLAN Identifier (12 Bits)
  802.1Q Max frame length: 1522 bytes

## Slide 160: Summary (1)
Static & Dynamic Channel Allocation
Multiple Access Protocols
  ALOHA
  Carrier Sense Multiple Access (CSMA/CD)
  Collision-Free Protocols
  Limited-Contention Protocols
  Wireless LAN Protocols (CSMA/CA)
Ethernet
  Ethernet Cabling
  Manchester Encoding
  Ethernet MAC Sublayer Protocol
  Binary Exponential Backoff Algorithm
  Fast Ethernet / Gigabit Ethernet /10 Gigabit Ethernet

## Slide 161: Summary (2)
Data Link Layer Switching
  Transparent Bridge
  Spanning Tree Bridges
  Remote Bridges
  Repeaters, Hubs, Bridges, Switches, Routers, Gateways
  Virtual LANs

## Slide 162: About ALOHA
Norman Abramson先后毕业于
Harvard大学、UCLA（加州大学
Los Angeles分校）、Stanford
大学，分别获学士、硕士、博士学位，毕业后在Stanford大学电子工程系任教。1967开始任Hawaii大学信息与计算机科学系教授，并从事通信理论研究，领导ALOHA系统研究项目，提出了著名的ALOHA多址通信协议和CRC（循环冗余校验）专利技术，并成功建立了世界上第一个数据通信网络ALOHANET，开创了计算机局域网和现代数据通信网，同时也首先实现了无线分组数据接入方法。

## Slide 163: About ETHERNET
1973年，为了实现几台电脑之
间的简单联接和信息交互，施乐
公司Palo Alto研究中心(PARC)
的研究员Bob Metcalfe描绘出了
大致的网络构想，并将这项技术
命名为“Ethernet”。当时的数据传输速率为
2.94Mbps，以太网就此诞生。